## Slide 1: AUTOMOTO
Group 16
Gregory Berkeley
Levi Lentz

## Slide 2: Acomplishments
1. Found Center of Gravity
    7 inches from the vertical
2. Developed Parts List and Spec Sheets
    Motors, Drivers, Controllers, Batteries
3. One microprocessor was missing a DC adapter from a 9V
    Soldered adapter to 9V leads giving the unit power
4. Set up simple Arduino commands

## Slide 3: Center Of Gravity

## Slide 4: Flaw with Previous Design
Only were using a proportional control with a gain of 1 for control steering
    No Integral or Derivative Control
Too slow of a time response to achieve stability
    Evidence found in videos from the previous team
Our Remedy
    Reconfigure the control system to incorporate PID controls

## Slide 5: Microprocessing
Currently using two Arduinos
    One to drive DC Motor
    Another to control stepper motor steering
Programming is very similar to C
    Task 1: Get sensor and Arduino to talk to each other and read data (ArduFlight)
    Task 2: Incorporate Stepper Motor to test time response

## Slide 6: Pulse Width Modulation

## Slide 7: Gull-Wing Training Wheels
Retractable “Training Wheels”
  Solve problem of starting the vehicle
  Will retract in a Gull-Wing manner
  Add to the rotational inertia of the bike
  Linear actuation via 4 bar link
    Or with simple rotation

## Slide 8: Future Work
Get electronics to work
  Independent high- and low-power systems
    Eventual integration of both systems
  Contact previous team for full wiring schematic
  Review previous code
Design “Training Wheels”
  Cad design
    Rotation or 4-bar link
  Integrate control into speed-sensing Arduino